## Slide 1
material steel
properties mises e 30000 nu 0.3 n_power 10 yld_pt 60.e10 $ linear-elastic
!
material rve_link
properties link stiff_link 1.0e10 mass_link 0.0
!
structure prism
!
number of nodes 35 elements 12
!
elements
1-8 type l3disop linear material steel order 2x2x2 bbar,
center_output short
9 10 11 12 type link2 material rve_link
!
*echo off
*input from file "coords_incid.inp"
*echo on
!
blocking automatic
!
*input from file ”rve_constraints.inp"
!
loading test
nonlinear
step 1 constraints 1.0
!
nonlinear analysis parameters $ only those really needed here
solution technique sparse direct
time step 1.0e06
maximum iterations 5 $ global Newton iterations
minimum iterations 1
convergence test norm res tol 0.001
batch messages off
trace solution on
!
output model flat patran convention text file "model"
!
compute displacements for loading test step 1
output wide strains 1-8
output wide stresses 1-12
output wide displacements 1-35
output flat text displacements $ for ParaView visualization
output flat text element stresses $ for ParaView visualization
!
stop