## Slide 1
*****************Start Step 1 -----------------------------------
*STEP,AMPLITUDE=RAMP,INC=1
Step 1
*STATIC
1,1
**
** Enforced strain tensor eps_ij (row-wise):
** row 1: 0.1 0.2 0.5
** row 2: 0.2 0.0 0.3
** row 3: 0.5 0.3 0.0
**
** Dummy strain mapping (eps_ij -> dummy_node, driver_node, dof):
** eps_11 -> dummy 28 u, driver 29 u
** eps_12 -> dummy 30 u, driver 31 u
** eps_13 -> dummy 32 u, driver 33 u
** eps_21 -> dummy 30 v, driver 31 v
** eps_23 -> dummy 34 v, driver 35 v
** eps_31 -> dummy 32 w, driver 33 w
** eps_32 -> dummy 34 w, driver 35 w
**
** --- BOUNDARY (absolute constraints) ---
*BOUNDARY
29, 1, 1, 0.1
31, 1, 1, 0.2
31, 2, 2, 0.2
33, 1, 1, 0.5
33, 3, 3, 0.5
35, 2, 2, 0.3
35, 3, 3, 0.3
1, 1, 1, 0.0
1, 2, 2, 0.0
1, 3, 3, 0.0
**
** Total zero absolute constraints (final, incl. implied): 3
** Total driver constraints (from eps_ij): 7
** Total MPC equations emitted: 39
** ------------------------------------------------------------
**
**
*node print,freq=1,nset=nall
u,
*el print,freq=1,elset=eall
s
*END STEP